## Slide 1: 4.0 Two Port Theory
EE1203 – Theory of Electricity
Prof J. Rohan Lucas
lucas@kdu.ac.lk
Department of Electrical, Electronic & Telecommunication Engineering
General Sir John Kotelawala Defence University
September 2020

## Slide 2: Learning Outcomes
t
On completion of module, student will be able to
LO1: Analyse the performances of AC circuits
Analyse circuits using nodal and mesh theory
LO2: Analyse two port networks using different models.
LO3: Analyse transfer functions of RLC networks for transients.
LO4: Analyse waveforms for its harmonics.
LO5: Perform calculations in three phase circuits including unbalanced waveforms.
Notes: .

## Slide 3: Port
Pair of nodes across which a device can be connected. Voltage is measured across pair of nodes.
Current going into one node is the same as the current coming out of the other node in the pair.
These pairs are entry (or exit) points of the network. Compare with an Airport or a Sea Port.
Entry and exit points to a country.
Planes that enter at a given port are the ones that take off from same port.
Landing
Take-off

## Slide 4: Systematic treatment of networks
Convenient to develop special methods.
Single-port linear active networks
  Thevenin’s or Norton’s equivalent circuit.
  Linear passive networks
  Study relative to a pair of designated ports.
Linear
Passive
Network
I1
I2
V1
V2
Port 1
Port 2

## Slide 5: Definitions
Driving point impedance is defined as ratio of applied voltage (driving point voltage) across a node-pair to the current entering at the same port.
[input impedance of network seen from particular port]
Driving point impedance at Port 1 = V1/I1
Driving point impedance at Port 2 = V2/I2
Driving point admittance is similarly defined as the ratio of the current entering at a port to the applied voltage across the same node-pair.
Driving point admittance at Port 1 = I1/V1
Driving point admittance at Port 2 = I2/V2

## Slide 6
Immittance is sometimes used to represent either an impedance or an admittance
Transfer impedance is defined as the ratio of the applied voltage across a node-pair to the current entering at the other port.
Transfer impedance = V1/I2 , V2/I1
Transfer admittance is defined as the ratio of the current entering at a port to the voltage appearing across the other node-pair.
Transfer admittance = I1/V2 , I2/V1

## Slide 7
Transfer Voltage gain (or ratio) is defined as the ratio of the voltage at a node pair to the voltage appearing at the other node-pair.
Transfer voltage gain = V1/V2 , V2/V1
Transfer Current gain (or ratio) is similarly defined as the ratio of the current at a port to the current at the other port.
Transfer current gain = I1/I2 , I2/I1

## Slide 8: Common Two-port parameters
External conditions of a two-port network can be completely defined by currents and voltages at the 2 ports.
A general two port network can be characterised by four parameters, derived from the network elements.
With symmetry, number of parameters will be reduced.
(a) Impedance parameters
(b) Admittance parameters
(c) Transmission Line parameters
(d) Hybrid parameters.

## Slide 9: (a) Impedance Parameters (z-parameters) or Open-circuit parameters
V1 = z11 I1 + z12 I2
If I2 = 0, then z11 = V1/I1
If I1 = 0, then z12 = V1/I2
Linear
Passive
Network
I1
I2
V1
V2
Port 1
Port 2

## Slide 10
It follows that,
,
,
,
z-parameters correspond to the driving point and transfer impedances at each port with the other port having zero current (i.e. open circuit).
 open circuit parameters.

## Slide 11: Example 3
I1
I2
V1
V2
Port 1
Port 2
Za
Zc
Zb
Find impedance parameters of the two port T – network.
With port 2 on open circuit
similarly with port 1 open,
z12 = Zb
z22 = Zb + Zc

## Slide 12: (b) Admittance Parameters (y-parameters) or Short-circuit parameters
Linear
Passive
Network
I1
I2
V1
V2
Port 1
Port 2
y11, y12, y21, y22 defined with either V1 or V2 zero.
y-parameters correspond to driving point and transfer admittances at each port with the other port having zero voltage (i.e. short circuit)  short circuit parameters.

## Slide 13: Example 4
I1
I2
V1
V2
Yb
Ya
Yc
I1
I2
V1
V2=0
Yb
Ya
Yc
with port 2 on short circuit
[Y] =
Find admittance parameters of the 2 port p–network.
y11 =
y21 =
= – Yb
= Ya + Yb

## Slide 14: (c) Transmission Line Parameters (ABCD-parameters)
Linear
Passive
Network
I1
I2
V1
V2
Port 1
Port 2
Parameters can be defined using either port 2 on short circuit or port 2 on open circuit.
In case of symmetrical system, parameter A = D.
For a reciprocal system, A.D – B.C = 1

## Slide 15: Example 5
I1
I2
V1
V2
Yc
Ya
Yb
Find ABCD parameters.
, B =
C =
and D =
[For symmetrical network, Ya = Yb , A = D].
=
=1
A =
A.D – B.C =

## Slide 16: (d) Hybrid Parameters (h-parameters)
Linear
Passive
Network
I1
I2
V1
V2
Port 1
Port 2
The hybrid parameter matrix may be written as
h-parameters can be defined as in other examples, and are commonly used in some electronic circuit analysis.

## Slide 17: Interconnection of two-port networks
(a) Series connection of two-port networks
Series properties are applied to each port
at port 1, Ir1 = Is1 = I1, and Vr1 + Vs1 = V1
at port 2 I r2 = Is2 = I2, and Vr2 + Vs2 = V2
[Z] = [Zr] + [Zs]
Linear
Passive
Network
r
Ir1
Ir2
Vr1
Vr2
Port r1
Port r2
Linear
Passive
Network
s
Is1
Is2
Vs1
Vs2
Port s1
Port s2
V2
V1

## Slide 18
(b) Parallel connection of two-port networks
Linear
Passive
Network
r
Ir1
Ir2
Vr1
Vr2
Linear
Passive
Network
s
Is1
Is2
Vs1
Vs2
V2
V1
I1
I2
at port 1, Ir1 + Is1 = I1, and Vr1 = Vs1 = V1
at port 2, I r2 + Is2 = I2, and Vr2 = Vs2 = V2
[Y] = [Yr] + [Ys]

## Slide 19: (c) Cascade connection of networks
Linear
Passive
Network
Is1
Is2
Vs1
Vs2
Port s1
Port s2
Linear
Passive
Network
Ir1
Ir2
Vr1
Vr2
Port r1
Port r2
Output of one network becomes input to next.
Ir2 = Is1 Vr2 = Vs1
,

## Slide 20: ABCD matrix of component networks
A =
B =
= Z, = 0
= 0, =Y
= 1, = 1
V1
V2
I1
I2
Z
V1
V2
I1
I2
Y
= 1, = 1
D =
C =

## Slide 21
I1
I2
V1
V2
Yb
Ya
Yc

Yb
Ya
Yc
In matrix form
=
, =
Consider example 5 again
=
Simplification of matrix product would give the same answer as in example 5.

## Slide 22: Input Impedance of Two-Port Network ZInput
ZInput depends on Input Port and on Load ZLoad
Port 1
Port 2
Z
4Z
Example:
With Load = 4Z at Port 2
ZInput, Port 1 = Z + 4Z//4Z = 3Z
With Load = 4Z at Port 1
ZInput, Port 2 = 4Z//(Z+4Z) = 2.222 Z
With Load = 6Z
ZInput, Port 1 = 3.4 Z, ZInput, Port 2 = 2.545 Z
Two-Port
Network
I1
I2
V1
V2
Port 1
Port 2
ZLoad
ZInput

## Slide 23: Image Impedance
Pair of Image impedances unique to Network
When load = ZI2 at Port 2
 Input = ZI1 at Port 1
Then with load = ZI1 at Port 1
 Input = ZI2 at Port 2
Best analysed by considering two such circuits in reverse cascade connection to reduce variables
Two-Port
Network
I1
I2
V1
V2
Port 1
Port 2
ZI1
ZI2
Two-Port
Network
I1
I2
V1
V2
Port 1
Port 2
ZI1
ZI2

## Slide 24: Example
ZI1
ZI1
Z
2Y
Z
ZI1
ZI2
Z
Y


ZI1
ZI2
Z
Y


ZI1
Z
Y



Reverse back-to-back networks are connected in cascade.
i.e. ZI1+ 2 ZI1ZY + 2 ZI12 Y = Z+ 2 Z2Y + 2 ZI1 ZY + Z + ZI1
gives 2Y ZI12 = 2Z (1+ZY) 
ZI2 = Y//(Z+ZI1) = =
(substitute for ZI1 and solve)

## Slide 25: Characteristic Impedance Z0
When 2-port network is symmetric, the image impedances become equal and is defined as Characteristic Impedance
Evaluated using ABCD or other 2 port parameters.
At Port 1, V1 = Z0 I1
At Port 2, V2 = Z0 I2
Matrix equation can be expanded as
V1 = A V2 + B I2 = A Z0 I2 + B I2 = (A Z0 + B) I2
I1 = C V2 + D I2 = C Z0 I2 + D I2 = (C Z0 + D) I2
 V1 = Z0 I1  (A Z0 + B) I2 = Z0 (C Z0 + D) I2
Two-Port
Network
I1
I2
V1
V2
Port 1
Port 2
Z0
Z0

## Slide 26
 A Z0 + B = Z0 (C Z0 + D)
 C Z02 + D Z0 = A Z0 + B, i.e. C Z02 + (D – A) Z0 – B = 0
For symmetrical network, A=D  Z0= B/C
Port 1
Port 2
½ Z
Y
½ Z
Example:
=
=
=  A=D=1+½ZY, B=Z(1+½ZY), C=Y
i.e. Y Z02 + (1+½ZY – 1 – ½ZY) Z0 – Z(1+½ZY) = YZ02 = Z(1+½ZY)


## Slide 27: End of Presentation